## Slide 1: Giraffes vs Fighter pilots

## Slide 2: High +Gz acceleration for fighter pilots

## Slide 3: Dangers
Cranial hypotension
Alternation to cardiovascular system
Impair cerebral blood flow
Impair visual ability
G-induced loss of consciousness

## Slide 4: Giraffe
Long neck -> huge hydrostatic force
Same as pilots when they lifting head
However they will NOT faint

## Slide 5: Intraocular pressure drops
Hydrostatic pressure = fluid density x acceleration x height of fluid colume
Normally: +1Gz, 30 cm between head and heart -> 22 mmHg
+2Gz => 44 mmHg, +4Gz -> 88 mmHg, worse when heart is lowered
Drops
  15 mmHg -> Visual impairment
  More -> Temporary unconsciousness

## Slide 6: Giraffe’s circulatory adjustments
+4Gz for human = +1Gz for giraffe
Maintain an optimal cerebral perfusion pressure (CPP)
Thick arterial walls and abundant connective tissues
  -> overcome 118mmHg
Valves in neck veins to prevent backflows of blood
  into brain
Non-collapsible ‘venous’ drainage channel to
enhence CPP
Legs are thin and the skin is non-distensible
  -> countermeasures

## Slide 7: Lessons to be learned for the pilots
Arterial pressure at head level must be maintained
Anti-G Straining Maneuver, AGSM
  Principle method for more than +5Gz
  Tensing leg, arm and abdominal muscles
Anti-G suit
  Pressurized with air to press the legs and abdominal region
  Create vasoconstriction
  Heart is elevated upward
Pressure breathing
  Wear a jerkin which is inflated to the same pressure as the mask
  counteract the high levels of pressures required

## Slide 8: More lessons
Muscular strength training
  10 – 12 weeks weight lifting
  -> increase 50% G-duration tolerance
Postural modification
  Decrease the vertical distance
  between brain and heart of the pilot
  F-16 fighter -> 30-degree seatback angle
  EMG-5 with prone position

## Slide 9: Conclusion
The pilots partially mimics some natural anatomical features of the giraffes
  AGSM -> increase arterial pressure at heart level
  Anti-G suit -> works like giraffe’s legs and skin
Giraffe should not fly!

## Slide 10: Thank you very much!