Mars Reconnaissance Orbiter
Payload: 139kg
Propulsion:	1175L, 1187kg Hydrazine monopropellent
6 large thruster, each 170N
6 medium thruster, each 22N
8 small thruster, each 0.9N

Mars Orbiter Mission
Payload: 13.4kg
Propulsion:	Liquid fuel engine. 852kg totally
1 large thruster, 440N
8 medium thruster, 22N

Mars express
Payload: 113kg
Propulsion:	267L, 595kg bipropellant
400N thruster

ExoMars Trace Gas Orbiter
Payload: 113.8kg
Propulsion:	bipropellent
424N thruster

Viking program
Payload: 91kg
Propulsion:	monopropellent
32N thruster

Monopropellent:
Exothermic chemical decomposition.
low-impulse rocket motor.
Pro: Simple and robust
Cons: Not as efficient as bipropellent

Bipropellent:
Liquid propellant
Pro: High density, small size. Use turbopumps to reduce the internal pressure. High mass ratio.
Cons: Complicate

The only one with a similar size as ours is the Mars Orbiter Mission. The 440N thruster is used for orbit rising and the 8 thrusters are used for orbital control. It uses bipropellent which we also can use for its efficiency. It uses MMH and N2O4 combination as its propellent. Both of them are very toxic and corrosive.